## Slide 1
ECE554 – Final Project Open Source IoT Connected Garage Controller
Authors
Daniel Zajac
Jackson Harmer
4/8/2019
ECE554 Embedded Systems
Final Project
1

## Slide 2
Agenda
Objective and Functional Description
Requirements
Design
  Process
  Hardware
  Software
Implementation
  Testing
  Performance
Performance
Accomplishments
Remaining Effort
Closing Remarks
References
4/8/2019
ECE554 Embedded Systems
Final Project
2

## Slide 3
Final Project Objective
Design an embedded real time system
Plan, Develop, Build and Test using waterfall development process
Develop requirements
Built on multi-tasked real-time system
Document design and software
Capture and evaluate system performance including:
  Timing
  Utilization
  Functional
Create presentation and Report
4/8/2019
ECE554 Embedded Systems
Final Project
3

## Slide 4
Automation System for consumer garage
Allows owner to:
  Monitor Temperature
  Open/close the door
  Monitor carbon monoxide (CO) levels
  Turn on and off external light
  Clear alarm
Connected as an IoT device
Can monitor via embedded display or web
Sensing detects obstacles in the door path
Triggers alarms if temp too high/low
Alarm if CO gets too high
4/8/2019
ECE554 Embedded Systems
Final Project
4
GarageRTC High Level Concept
Connected GarageRTC Embedded System High Level Concept

## Slide 5
Planning
The project timeline was developed based on team availability and delivery milestones
A Gantt chart was developed to outline the major phases of project development
4/8/2019
ECE554 Embedded Systems
Final Project
5

## Slide 6
Requirements From Proposal
The project proposal identified 7 Key requirements:
  ECE554-REQ-001 – Manual Interface Switches
    The system shall provide, at a minimum, manual interface switches for Alarm Silence, Door, Stop, and Light.
  ECE554-REQ-002 – Local Display
    The system shall have a digital display mounted to the main controller.
  ECE554-REQ-003 – Light Control
    The system shall provide the ability to digitally switch the following:
      Latching switch a single mains powered LED bulb
      Electrically isolated momentary switch that interfaces with the opener control
      Latching switch an alarm.
  ECE554-REQ-004 – Sensing Requirements
    The system shall sample the following sensors:
      mbient temperature of the garage
      CAarbon monoxide level
      Door position, at a minimum Open or Closed
      Detect obstacle beneath the closing door
4/8/2019
ECE554 Embedded Systems
Final Project
6

## Slide 7
Requirements From Proposal
  ECE554-REQ-005 – IoT Connectivity
    The system shall connect to the web server via Wifi, serial, ethernet or other suitable protocol. The system shall make available to the web server the following information:
      Sensor readings
      Door status
      Error status
    The system shall receive the following information from the server:
      Door command
      Light command
    The system shall inform the web server upon completion or failure of any command.
  ECE554-REQ-006 – Web Service
    The system shall host a page that displays the information on the local display.
4/8/2019
ECE554 Embedded Systems
Final Project
7

## Slide 8
Timing Requirements
4/8/2019
ECE554 Embedded Systems
Final Project
8
ECE554-REQ-007 – Timing Requirements
  The system shall meet the following timing metrics as defined in the table below:
Parameter | Timing Requirement
Local Display Update | Every 500 mS or better
Obstacle Detection | Toggle the opener control within 150 mS from sensor detection
Limit Switch Detection | Toggle the opener control within 150 mS from sensor detection
Door movement Response | Toggle the opener control within 300 mS from button press
Light Response | Latch the light control within 300 mS from button press
Post to Server interval (Idle) | Post to the server every 5000 mS
Event push to server | Post data to the server within 500 mS from the event.
Check Server for messages | Check for remote messages every 1000 mS or better

## Slide 9: Waterfall Design Process
Concept
Requirement
Design
Implement
Test
Maintenance
Project Proposal Paper
System Block Diagram
High Level Design
Build HW/SW, Integrate
Functional Testing
Test Procedure
Unit Testing
Daft Manual
Final Manual
Report
Future
Improvements

## Slide 10
Design
High Level Design
Partitioning
Embedded Software Design
Embedded Hardware Design
Connected Software Design
4/8/2019
ECE554 Embedded Systems
Final Project
10

## Slide 11
High Level Design
Reviewed functional requirements from proposal
  Interface switches for Alarm Silence, Door, Stop, and Light
  Digital display mounted to the main controller
  Able to digitally switch mains powered LED bulb, door button, alarm
  Detect temperature, Carbon monoxide, door position, obstacle beneath door
  IoT connectivity to send/receive from a web server
The timing requirements and sensor input types were assessed
A block diagram of the system was constructed from the requirements
4/8/2019
ECE554 Embedded Systems
Final Project
11

## Slide 12
GarageRTC System Block Diagram
4/8/2019
ECE554 Embedded Systems
Final Project
12

## Slide 13
System Partitioning
4/8/2019
ECE554 Embedded Systems
Final Project
13
The system was then partitioned
A structure chart was created
  Shows logical relationships within the system
  Major subsystems for embedded and web
  Sub functions for each subsystem
Web subsystem
  Developed in HTML, JavaScript, and Python
  Will interact with controller through UDP
  Defined a standard interface for messaging
Embedded subsystem
  Can be developed separately in C/C++
  Can produce/consume UDP Data
  Will execute multiple tasks in Real Time
GarageRTC Structure Chart

## Slide 14
Embedded Task Decomposition
Isolated behaviors for each part of the system and assigned priorities
Sensor was oversampled to ensure each task received freshest value
Grouped behaviors into compatible tasks and assigned RTOS Priority
4/8/2019
ECE554 Embedded Systems
Final Project
14
Behavior | Priority | Frequency | Group Task | RTOS Priority
Reading and converting sensor input | High | 100 Hz | TaskReadSensors | 3
Door Control | High | 10 Hz | TaskStateMachines | 2
Alarm Control | Medium | 10 Hz | TaskStateMachines | 2
Light Control | Low | 10 Hz | TaskStateMachines | 2
Network | Low | 1 Hz | TaskNetwork | 1
Display | Low | 2 Hz | TaskUpdateDisplay | 1
WatchDog Collection | Low | 0.7 Hz | TaskIdle | 1

## Slide 15
Used to produce latching relay
Prevents unwanted behavior:
  Relay chatter from long presses
  Glitched presses resulting fast toggle
Idle – Waiting for an edge
Press – Saw an edge, keep sleeping while the button is held. Turn light on.
Release – Button released
2nd Press – Keep sleeping while button is held. Turn light off.
4/8/2019
ECE554 Embedded Systems
Final Project
15
Light Toggle State Machine
State machine to create latched relay behavior from button presses

## Slide 16
4/8/2019
ECE554 Embedded Systems
Final Project
16
Door Control State Machine
Door control state machine to run opener output
Used to produce timed pules simulating door button presses
  Idle – Waiting for a door command
  Start – Saw a door command. Close the door button relay. Idle for time t or a Stop command
  Moving – Door is moving, wait for a limit switch or Stop command.
  Stopping – Close the door button relay for time t, stopping the door. Then return to Idle.

## Slide 17
Used for control the system alarm state
  Idle – Monitor for temp and CO within limits.
  Alarm – When outside limits, set the alarm state. If the value falls within limits + a hysteresis value, clear the alarm. If someone presses the Alarm silence button, silence the alarm but maintain the state.
  Silenced – The alarm relay is released but the alarm state is maintained till the levels are acceptable
4/8/2019
ECE554 Embedded Systems
Final Project
17
Alarm State Machine
Alarm State Machine maintains the system Alarm State and relay.

## Slide 18
The watchdog collects bits from each running task
  T1 completes, requests exclusive access to the watchdog bowl. Then writes it’s bit and releases.
B. - D. Each task takes it’s turn writing their bits into the bowl.
  The WatchDog task (TaskIdle) grabs the bowl and checks for 0xF.
  If all bits are in the bowl, the WD timer is reset
  TaskIdle resets the bowl for the next round.
4/8/2019
ECE554 Embedded Systems
Final Project
18
Multi-Tasked WatchDog Design
Messaging Interface between Web and Embedded System

## Slide 19
In the event a process stalls
  Task 1 fills the bowl
  Task 2 is stalled, does not set bit
  Task 3 sets bit
  Task 4 sets bit
  The TaskIdle fetches the bowl
  Missing bit does not pet the dog
  The TaskIdle clears the flags
  After the Watch Dog timer exhausts, the system is reset
Can be extended to support checking deadlines
4/8/2019
ECE554 Embedded Systems
Final Project
19
WatchDog Reset Example
Task 2 is stalled, missing it’s write to the WatchDog Bowl eventually triggering a system reset

## Slide 20
Web Data Flow Diagram
4/8/2019
ECE554 Embedded Systems
Final Project
20
Read Network Packet
Web Status Page
Web Button Presses
Network Interface
Interval Timer
Combine Command into Packet
Process
JSON Data
Store to Python
Data structure
Jscript
Renders Page
Jscript
Raises Signal

## Slide 21
Embedded Hardware Design
Reviewed the requirements
Selected hardware based on interface requirements
Made design decisions for aspects not identified by requirements, selected:
  WiFi for communication to the web server
  Laser/receiver for obstacle detection
  I2C for display communication
  Reed switches for up/down limit switches
  Modular relay board for button, alarm, and light switching
Made software design decisions, selected:
  C/C++ for the development language
  Arduino IDE for development environment
  FreeRTOS for RTOS support
4/8/2019
ECE554 Embedded Systems
Final Project
21

## Slide 22
Embedded Hardware Design
For the system controller, an ESP32 was selected as it offers:
  Native WIFI integration
  Multiple cores
  Incredibly fast 80 MHz+
  Excellent support for peripherals
    I2C LCD Drivers
    UDP Server/Client capabilities
    FreeRTOS support
  Supports multiple IDEs (Arduino, EspressIF, Eclipse)
  Good community documentation and support
Using the ESP32-NodeMCU development module, a schematic was created
4/8/2019
ECE554 Embedded Systems
Final Project
22

## Slide 23
Schematic
4/8/2019
ECE554 Embedded Systems
Final Project
23

## Slide 24
The ESP32 is a series of system-on-a-chip micro-controllers that utilizes the Tensilica Xtensa microprocessor
The ESP32 can be programmed in C, C++, MicroPython, or Xtensa Assembler
Most development boards also include a USB to serial interface to allow for easy re-programming and serial monitoring
Supports the use of Arduino tools and libraries
4/8/2019
ECE554 Embedded Systems
Final Project
24
The Micro-Controller: ESP32
The ESP32 Micro-Controller

## Slide 25
The ESP32’s features include:
  Dual-core 32-bit processor clocked at 240 MHz
  Ultra-low power co-processor (for sleep modes, interrupts)
  25 Digital GPIO, 6 Analog Input, and 2 Analog Output pins
  3 UART, 3 I2C, and 2 SPI devices
  Cryptographic and security ASICS
  4 MB of Flash, with 520 KB of SRAM
  Built in 802.11n Wi-Fi and Bluetooth LE
  Software, hardware, and timer interrupts
  Multiple tiers of “sleep mode”
4/8/2019
ECE554 Embedded Systems
Final Project
25
ESP32 Architecture
The ESP32 Micro-Controller Architecture [1]

## Slide 26
ESP32 Memory Map
4/8/2019
ECE554 Embedded Systems
Final Project
26
The ESP32 Micro-Controller Memory Map [2]

## Slide 27
Laser diode module
Laser detector – Obstacle Detection
MQ-7 CO detector
Reed Switch – Door Limits
4x20 Character I2C Display
10K Glass bead thermistor – Temp
PCB push button – Interface switches
4x opto-isolated Relay module
4/8/2019
ECE554 Embedded Systems
Final Project
27
Remaining Hardware Selected
Components used in construction of the embedded system
A
B
C
D
E
F
G
H

## Slide 28
Software and FreeRTOS
Selected for broad hardware support and native ESP32 libraries
Based on C/C++
Is a free and open source real-time OS kernel for embedded systems
Supported by many platforms and CPU architectures
Well researched scheduling and extensible for near hard real-time [4]
Provides a way for interfacing with the hardware to provide access to:
  Multi-threading
  Task scheduling
  Mutexes, semaphores, and locks
  Interrupts
  Software timers
  Dynamic memory allocation
4/8/2019
ECE554 Embedded Systems
Final Project
28

## Slide 29
4/8/2019
ECE554 Embedded Systems
Final Project
29
FreeRTOS Scheduling Options
By default, FreeRTOS uses a hybrid of priority-based and round-robin scheduling
The highest priority task is granted CPU time first
Equal priority tasks go into round-robin scheduling
Can be configured to use either preemptive or cooperative
Cooperative being good for low-power applications (doesn’t rely on system ticks)
Hybrid Preemptive and Cooperative scheduling [5]

## Slide 30
Embedded Tasks
Multiple tasks can share CPU time on both cores
Tasks include:
  TaskReadSensors - Reading and converting sensor input
  TaskStateMachines - Door, Alarm, and Light Control
  TaskNetwork – Network receiving and sending
  TaskUpdateDisplay – Update LCD Display
  TaskIdle – WatchDog Collection
4/8/2019
ECE554 Embedded Systems
Final Project
30

## Slide 31
2/4/2019
ECE554 Embedded Systems
Final Project
31
Networking Tasks
Messages are periodically sent from the controller to the web server
  Messages are in a JSON serialized format
  Messages are sent over UDP
  Messages are encrypted using private and public keys
Messages are received asynchronously from the web server
  Also in JSON format, sent over UDP, and encrypted
  Messages from web server are treated as high priority software interrupts

## Slide 32
Implementation
Hardware Implementation
Embedded Software Implementation
Networked Software Implementation
Integration
Debugging
4/8/2019
ECE554 Embedded Systems
Final Project
32

## Slide 33
4/8/2019
ECE554 Embedded Systems
Final Project
33
Display
Optical Detector
Interface Buttons
CO Detector
Relays
ESP32
Debug
Limit Switches
Embedded Construction

## Slide 34
The web server hardware is non-specific
For this project, a Raspberry Pi was used
  Offers compact footprint, with fast ARM processor
  Runs Debian based Linux
Pi was loaded with Python and Flask
Pi communicates with controller using UDP (communication over wired protocols such as SPI, UART, or I2C is also possible)
Web Server Construction
Raspberry PI running the Server Software for this Project
4/8/2019
ECE554 Embedded Systems
Final Project
34

## Slide 35
Web Server Software
The web server running on the Raspberry Pi uses the Flask web framework
  Written in Python, allows for hosting small to medium web apps on low-powered devices
  Serves HTML, CSS, and JavaScript using Jinja templates
  Supports plugins such as WebSocket API
  Allows for interaction with the host OS and hardware via Python
  Supports hot reloading
WebSockets are used to allow for asynchronous programming
  jQuery and JavaScript WebSocket API run on client machine and connect to Flask WebSocket API running on server
  Client can issue a command to use a callback function on the server computer
  This can be used to trigger events such as sending UDP messages to the controller or changing settings
4/8/2019
ECE554 Embedded Systems
Final Project
35

## Slide 36
Web Server Software
4/8/2019
ECE554 Embedded Systems
Final Project
36

## Slide 37
Testing
4/8/2019
ECE554 Embedded Systems
Final Project
37
Unit Testing
Integration Testing
System Testing
Performance Testing

## Slide 38
Test Plan and Cases for Embedded
Unit testing
  Individual hardware components – Ensure board is functioning
  Each tasks with individual tests for:
    Each task state machine
    Each function
    Reading/writing shared variables
    Feeding the Watchdog
  Connecting, sending, and receiving network traffic
Integration testing when merging in each task
Timing requirements testing
Functional testing of the embedded system installed
2/4/2019
ECE554 Embedded Systems
Final Project
38

## Slide 39: Test Plans
# | L | Description | Tests function:
1W | U | Flask | Flask framework
2W | U | SocketIO | SocketIO interactivity
3W | U | Database | Save/Retrieve data
4W | U | Network | Receive/Send UDP
5W | I | Settings Page | Settings functions
6W | I | Status Page | Status page
7W | I | Network Commands | Send/Receive commands
8W | I | Embedded | Embedded send/receive
9W | F | Functional | System performance installed
# | L | Description | Tests function:
1E | U | Board functional | Basic I/O, IDE, toolchain
2E | U | Display | LCD Driver, Text, Display Task
3E | U | A/D sensing | AD conversion, scaling
4E | U | CO | CO sensor, Calibration
5E | U | Temperature | Temperature, Calibration
6E | U | Relay | Relay module, I/O driver
7E | U | Limit Switches | Switch input
8E | U | Buttons | Button input
9E | U | Network | Associate, receive, send UDP
10E | U | Alarm Logic | State machine for Alarm control
11E | U | Light Logic | State machine for Light control
12E | U | Door Logic | State machine for Door control
13E | U | FreeRTOS | Scheduler, library compatibility
14E | U | Shared Memory | Globals, mutexes, semaphores
15E | I | Network Cmds | Send/Receive commands
16E | I | Display | Integrate all display elements
17E | F | Benchtop Sim | System performance on bench
18E | F | Functional | System performance installed
19E | A | Timing | System response time
Embedded System Test Plan
Web System Test Plan

## Slide 40
Embedded Testing
Unit tests were built to execute specific hardware
  Tests performed at the completion of each feature
  Component testing with dummy data
  Simulators used to supply test network data
  Checklists and tables used to track integration progress
Integration Testing
  Software then merged into the trunk
  Periodic regression testing performed during integration
  Periodic testing between stable releases of web and embedded
4/8/2019
ECE554 Embedded Systems
Final Project
40

## Slide 41
ESP32
  Tests for UDP message integrity (sending and receiving)
  Tests for UDP timing
  Tests for Wi-Fi connection and re-connection
Web Server
  Tests for UDP message integrity (sending and receiving)
  Tests for UDP timing
  Tests for HTTP communications
  Tests for asynchronous WebSocket behavior and responsiveness
4/8/2019
ECE554 Embedded Systems
Final Project
41
Networked Unit Testing
Unit tests are created for both the ESP32 controller and Raspberry Pi server

## Slide 42: Acceptance Test Installation

## Slide 43
For each test
  All other tasks disabled
  Debug port attached to an oscilloscope
  Debug pin set high on task wake-up
  Set low after last instruction
Captured timing on scope – Best possible timing
4/8/2019
ECE554 Embedded Systems
Final Project
43
Non-preempted Timing
Pseudo code used for unprempted task timing
Captured Non-preempted Timing for the TaskReadSensors – 29.5uS

## Slide 44
Non-preempted Timing
4/8/2019
ECE554 Embedded Systems
Final Project
44
The non-preempted timing was recorded for each task
The cycle timing for scheduler was also captured
Cycle times were found to be exceptionally accurate
Display task was found to be stand out slow
  Research revealed lots of delays in the I2C library
  Most likely to make the library compatible with wide variety of displays
Task | Function | Priority | Freq | F Meas | t
TaskReadSensors | Reading and converting sensor input | High | 100 Hz | 100 Hz | 29.5 uS
TaskStateMachines | Door, Alarm, and Light Control | High | 10 Hz | 10 Hz | 1.41 uS
TaskNetwork | Network | Low | 1 Hz | 1 Hz | 1.015 – 2.015 mS
TaskUpdateDisplay | Display | Low | 2 Hz | 2 Hz | 39 mS
TaskIdle | WatchDog Collection | Low | 0.7 Hz | Varies | 1.05 uS

## Slide 45
Utilization Calculation
Calculated worst case utilization
U = 8.3% - Extremely underutilized
Overpowered but ESP32 has other benefits!
4/8/2019
ECE554 Embedded Systems
Final Project
45
Task | F Meas | ei | pi | ei/pi
TaskReadSensors | 100 Hz | 29.5 uS | 0.01 | 0.00295
TaskStateMachines | 10 Hz | 1.41 uS | 0.1 | 1.41E-05
TaskNetwork | 1 Hz | 2.015 mS | 1 | 0.002015
TaskUpdateDisplay | 2 Hz | 39 mS | 0.5 | 0.078
TaskIdle | Varies | 1.05 uS | 0.666667 | 1.58E-06
 |  |  | Total: | U = 0.083

## Slide 46
Flash and Memory
Current application uses 720 kB bytes (54%) of program memory 1.31 MB
Without Networking and UDP libraries, application consumed ~15%
  Network stack and UDP messaging consumes ~524 kB
  Almost 40% of program memory!
Global variables use 38kB (11%) of dynamic memory
  290 kB for local variables
  Includes individual task stacks
4/8/2019
ECE554 Embedded Systems
Final Project
46

## Slide 47
All tasks were returned to active scheduling
Added second scope channel to ensure task priority was being enforced
Timing remeasured with preemption and compared
Concurrent Execution Timing
4/8/2019
ECE554 Embedded Systems
Final Project
47
The scheduler is stealing time from the longer TaskUpdateDisplay to ensure TaskReadSensors is executed on schedule.
Channel 1 - TaskReadSensors
Channel 2 – TaskUpdateDisplay

## Slide 48
Preempted Timing
4/8/2019
ECE554 Embedded Systems
Final Project
48
The following table shows the preempted timing
Of particular note
  Display timing got much worse ~ 6x slower
  Most others stayed about the same
  Further investigation on the display task is required
Task | Function | Priority | Freq | F Meas | t w/o PE | T with PE
TaskReadSensors | Reading and converting sensor input | High | 100 Hz | 100 Hz | 29.5 uS | 29.5 uS
TaskStateMachines | Door, Alarm, and Light Control | High | 10 Hz | 10 Hz | 1.41 uS | 1.38 uS
TaskNetwork | Network | Low | 2 Hz | 2 Hz | 1.015 – 2.015 mS | 2.02 mS
TaskUpdateDisplay | Display | Low | 2 Hz | 2 Hz | 39 mS | 274 mS
TaskIdle | WatchDog Collection | Low | 0.7 Hz | Varies | 1.05 uS | 1.05uS

## Slide 49
Response Timing
4/8/2019
ECE554 Embedded Systems
Final Project
49
Timing measured using oscilloscope
CH1 Connected to button input, CH2 to relay output
Measured 10 transitions, and averaged. Max was no more than 86.2, average 58.6
Web timing and display timing based on cycle times.
All timing requirements per original proposal met
Parameter | Timing Requirement | Measurement | P/F
Local Display | Every 500 ms or better | 500 ms | P
Obstacle Detection | Toggle opener within 150 ms from detection | < 86.2 ms | P
Limit Switch | Toggle opener within 150 ms from detection | < 86.2 ms | P
Door movement | Toggle opener within 300 ms from press | < 86.2 ms | P
Light | Latch light within 300 ms from press | < 86.2 ms | P
Idle Post to Server | Post to the server every 5000 ms | 500 ms | P
Event push to server | Post to the server within 500 ms from event. | <= 500 ms | P
Check Server | Check remote messages every 1000 ms | 500 ms | P

## Slide 50: Comparison with other Products
Performed market survey
  Chamberlain MYQ-G0301
  Aladdin Connect
  Garage Door Buddy
  Go Control GD00z-4
Generated Matrix for comparison
Considered
  Connectivity
  Digital Assistant Compatibility
  Sensing and Control
  Local Control Features
  Openness of Design

## Slide 51: Comparison with other Products
Feature | MYQ-G301 | Connect | Door Buddy | GoControl | GarageRTC
Connectivity |  |  |  |  | 
WiFi | ✔ | ✔ | ✔ |  | ✔
Bluetooth |  |  |  |  | 1
ZWave |  |  |  | ✔ | 
Digital Assistant |  |  |  |  | 
Alexa |  |  |  |  | 2
Google |  |  |  |  | 3
Siri |  |  |  |  | 3
Sense/Control |  |  |  |  | 
Aux Control | 4 |  |  |  | ✔
Amb. Temp |  |  |  |  | ✔
Amb. CO |  |  |  |  | ✔
Door Position | ✔ | ✔ | ✔ | ✔ | ✔
Local Control |  |  |  |  | 
LCD Display |  |  |  |  | ✔
Door | ✔ | ✔ | ✔ | ✔ | ✔
Aux/Light |  |  |  |  | ✔
Open Source |  |  |  |  | 
Web App |  |  |  |  | ✔
FOSS |  |  |  |  | ✔
Published API |  |  |  |  | ✔
HW Schematic |  |  |  |  | ✔
Universal |  |  | ✔ | ✔ | ✔

## Slide 52
Comparison with other Products
Findings:
  GarageRTC mostly comparable with similar products
  Open Source means could extend to include missing features
Security not considered
  Most other products claimed security
  Not forthcoming with mechanism or implementation
  Other researchers had found problems with their security [6] [7]
  Omitted since offering unknown quality of security could not be compared
Open source could help here
  Open publishing of security mechanisms could lead to community improvements
  Security through obscurity is not viable solution
4/8/2019
ECE554 Embedded Systems
Final Project
52

## Slide 53
Accomplishments
Embedded Hardware Development:
  System is assembled and complete
  Individual hardware tests pass
  Test system is reliable and consistent
Embedded Software Development:
  Embedded system development is mostly complete
  Web connectivity needs integration
Web Software Development:
  Web receiver/transmitter are working with simulators
  Completed interface and integration
Testing
  Embedded system has completed unit and integration tests
  Timing testing is nearly complete
  Hardware installation for functional tests
4/8/2019
ECE554 Embedded Systems
Final Project
53

## Slide 54
Closing Remarks
It was a challenge to integrate the IoT and embedded elements
All materials in GitHub project: https://github.com/jharmer95/Garage-RTC
ESP32 performance far exceeds system requirements but:
  Integrated Wi-Fi makes connectivity possible
  Exceptional library support made integration faster
  FreeRTOS support made multitasking easier
Possible Future Improvements:
  H-Bridge motor drive for direct door control
  Encryption between controller and server
  Develop Android application with notification support
  Add Built-In-Test (BIT)
  Front panel guided menus for set-points, settings, AUX control
  Support for viewing CCTV feed connected to web server
4/8/2019
ECE554 Embedded Systems
Final Project
54

## Slide 55
Video
On YouTube Here: https://www.youtube.com/watch?v=IwsxoqProoo
4/8/2019
ECE554 Embedded Systems
Final Project
55

## Slide 56
References
[1] Explore Embedded, "Overview of ESP32 features. What do they practically mean?," Explore Embedded, 8 April 2019. [Online]. Available: https://www.exploreembedded.com/wiki/Overview_of_ESP32_features._What_do_they_practically_mean%3F.
[2] Amazon Web Services (AWS), "FreeRTOS - Why Use an RTOS Kernel?," Amazon Web Services (AWS), 8 April 2019. [Online]. Available: https://www.freertos.org/tutorial/solution1.html.
[3] Rapita Systems, "What are “co-operative” and “pre-emptive” scheduling algorithms?," Rapita Systems, 2019 April 2019. [Online]. Available: https://www.rapitasystems.com/blog/cooperative-and-preemptive-scheduling-algorithms.
[4] I. V. Cretu, V. M. Micea and S. C. Stangaciu, "Hard real-time execution environment extension for FreeRTOS," in IEEE International Symposium on Robotic and Sensors Environments (ROSE), Timisoara, Romania, 2014.
[5] Amazon Web Services (AWS), "FreeRTOS Project," Amazon Web Services (AWS), 8 April 2019. [Online]. [Accessed 2019].
[6] Margulies, "Garage Door Openers: An Internet of Things Case Study," IEEE Security & Privacy, 2015.
[7] C. Goudie and R. Weidner, "Home hackers: Digital invaders a threat to your house," ABC 7 News, Chicago IL, 12 February 2015.
4/8/2019
ECE554 Embedded Systems
Final Project
56

## Slide 57
Questions?
Daniel A. Zajac
danzajac@umich.edu
(313) 655-7533
4/8/2019
ECE554 Embedded Systems
Final Project
57
Jackson Harmer
jharmer@umich.edu
(810) 941-2280